## Slide 1: Smart Link Selection
By
Andrey Shamis
And
Ilia Gaisinsky
הצגת הפרויקט

## Slide 2: Project Goal
Creation of WiFi simulator in order to develop Smart Link Selection Algorithms

## Slide 3: Project Overview
Simulator
  Design
  Supported Protocols
  Used algorithms
  Usability
SLS Algorithm
  Algorithms flow
  Statistic
  Conclusion

## Slide 4: Simulator - Design
Medium infrastructure.
RF devices
Packets
GUI
Support of two different data links:
  BSS
  TDLS

## Slide 5
Rx/Tx emulation over Medium
Radius Calculation
Multiple Channel support
Dual Band support
RSSI Calculation
Transmission Data Rate
Noise Simulation
Tx opportunity
Acknowledgment
MAC resolution

## Slide 6: RF Devices UML

## Slide 7: RF Devices
AP
    Able to transfer any kind of packets without any code change
    Buffers packet for each STA
  STA
    Preferred (best) Channel finding for TDLS
    Stream handler / File to Packets division and restoration

## Slide 8: Packets UML

## Slide 9: GUI
DEMO
Notes: Easy access to get all simulated information
Ability to move objects on board - Drag & Drop
Creation of RF device
Random simulation
Static simulation
Station info form :
  Statistic
  Logs
  Station configuration and overview
  Configurable dump of STA object
AP info form – provide basic configuration
Saving and Load current simulation into file

## Slide 10: Supported Protocols
IEEE80211
  Passive scan
  Beacon sending
  Acknowledgment
  Connect/Disconnect flow
  Keep Alive mechanism
  Support of standards - Band A, Band N
  Connection establishment negotiation
  Base Service Set
  Tunneled Direct Link Setup

## Slide 11: Used Algorithms
Calculation of Received Signal Strength Indication (RSSI)

## Slide 12: Used Algorithms
Signal to Noise Ratio (SNR) – Packet Loss
Chart: Probability of loss packet
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
Probability % | 0 | 0 | 0 | 0.015 | 0.0298 | 0.0575 | 0.0843 | 0.1048 | 0.1367 | 0.1655 | 0.1896 | 0.2121 | 0.2438 | 0.2709 | 0.2898 | 0.3165 | 0.3423 | 0.3761 | 0.4023 | 0.4291 | 0.4618

## Slide 13: Used Algorithms
Calculation of transmit rate regarding to RSSI
Chart: RATES
| 20MHz | 40MHz | 20MHz | 40MHz | 2.4GHz | 2.4GHz | 5GHz | 5GHz
-61 | 144 | 300 | 144 | 300
-62 | 144 | 300 | 130 | 270
-63 | 144 | 300 | 115 | 240
-64 | 144 | 300 | 115 | 240
-65 | 130 | 270 | 115 | 240
-66 | 115 | 240 | 115 | 240
-67 | 115 | 240 | 86 | 180
-68 | 115 | 240 | 86 | 180
-69 | 115 | 240 | 86 | 180
-70 | 86 | 180 | 86 | 180
-71 | 86 | 180 | 57 | 120
-72 | 86 | 180 | 57 | 120
(Kbps)
(DBm)

## Slide 14: Used Algorithms
Calculation of transmit rate regarding to RSSI

## Slide 15: Smart Link Selection
We have developed 2 different SLS algorithms:
  Null Data Packet Based Algorithm
  Window Based Algorithm

## Slide 16: Null Data Packet
Sampling by sending packet on TDLS link and then on BSS link
Each channel sends X packets
The sampling is performed every Y seconds
Sending packets are in parallel to sending data

## Slide 18: Null Data Packet
Advantages
  Small packet size – not overload the network
  Simple
  Independent on sending actual data
Disadvantages
  While sampling, affects on sending actual data
  Independent on sending actual data

## Slide 19: Window Based Algorithm
Parameters
  Cycle size (NUM of Packets)
  Window Size (Percent of Cycle)
  Window boundaries (MIN, MAX)

## Slide 20: Window Based Algorithm

## Slide 21: Window Based Algorithm

## Slide 23: Window Based Algorithm
Advantages
  Uses actual Data Packets for sampling – No Overhead
  Dynamic increase/decrease samples window size
  Can be integrated in the MAC layer (Wi-Fi Driver) or on the device it self (Firmware)
  Samples count parameter might be controllable regarding traffic load.
Disadvantages
  Not end-to-end estimation

## Slide 24: Comparison of Algorithms
Simulation of two different scenarios :
  Better to use BSS
  Better to use TDLS
Comparison of Speed and Retransmission rate of both scenarios

## Slide 25: Simulation Results
BSS better
Distance | AP | STA 1 | STA 2
AP | 0 | 50 | 55
STA 1 | 50 | 0 | 80
STA 2 | 55 | 80 | 0
Chart: Speed MBps
| BSS | TDLS | SLS NullData | SLS Window
Speed Mbs | 17 | 6 | 8 | 13
Chart: Retransmission
| BSS | TDLS | SLS NullData | SLS Window
Retransmission | 110 | 200 | 190 | 125

## Slide 26: Simulation Results
TDLS better
Distance (meters) | AP | STA 1 | STA 2
AP | 0 | 92 | 93
STA 1 | 92 | 0 | 5
STA 2 | 93 | 5 | 0
Chart: Speed MBps
| BSS | TDLS | SLS NullData | SLS Window
Speed Mbs | 2 | 50 | 30 | 31
Chart: 
| BSS | TDLS | SLS NullData | SLS Window
Retransmission | 598 | 11 | 40 | 37

## Slide 27: Management Tools
https://github.com/AndreyShamis/sls/
http://jenkins.dhs01.com/
Repository
Auto compiler

## Slide 28: Demo
Simulator

## Slide 29: Questions

## Slide 30: Bibliography
IEEE 802.11 SPEC - WiFi
IEEE 802.11z SPEC - TDLS
Wireless Rate Control Algorithms
DDRS
MAC rate control algorithm
WiFi Alliance
WiFi Direct - http://linuxwireless.org/
A Routing Algorithm for Wireless Ad Hoc Networks with Unidirectional Links
Wikipedia - Wireless network
Our web site for project: http://wiki.dhs01.com/

## Slide 31: Bibliography
Signal-to-noise ratio
RSSI vs Data rates
Configure 802.11n on the WLC
Coverage or Capacity - Making the best use of 802.11N